## Slide 1: Energy Security
Mark Barrett
Mark.Barrett@ucl.ac.uk University College London

## Slide 2: Homo sapiens
Energy and material demands
  tissue formation and maintenance
  keeping warm, keeping cool
  movement
  information processing
Energy from oxidising carbon in food, renewable biomass
Refined control systems to minimise energy and water consumption
Comfort is when energy and water consumption is minimised
Most exosomatic services (buildings, transport) designed to minimise endosomatic energy consumption, to achieve comfort – this is a basic driver of energy demand
e.g. 10% UK energy & emissions to keep warm air next to skin

## Slide 3: Leviathan today
Leviathan’s diet
50 times as much energy per person as direct human needs (UK)
Diet mainly finite fossil carbon fuels
Problems with the diet
Impending food shortage
Global stores of fossil carbon :
  Oil, gas about 50 years reserves
  Coal some centuries
Global warming because of waste gases
Temperature rise of more than 2 C, or 0.2 C per decade, will devastate human and other ecosystems

## Slide 4: History and future of people and energy?
1950 to 2100. Transition fossil to renewable
0 to 2500. Renewable => fossil => renewable. Steady state humanity?
1800 to 2300. . Transition fossil to renewable

## Slide 5: Security: framing issues
Energy security can be defined as:
The provision of adequate energy services for human wellbeing that are:
Affordable
Reliable
Sustainable

## Slide 6: Security: planning for a renewable future

## Slide 7: Security: energy services
A hierarchy of importance for energy services can be constructed:
Core services which it is immediately dangerous to interrupt
  water and food supply
  domestic space heating, lighting
  emergency services; health, fire, police
Intermediate importance. Provision of social services and short-lived essential commodities
Lower importance. Long-lived and inessential commodities e.g. foreign holidays
Part of energy security or emergency planning is for these energy services to degrade gracefully to the core.

## Slide 8: Energy service chain security
Chain to deliver energy services with demand and supply spatiotemporal distributions, some weather dependent
Probability of service failure is a function of failure in individual components and their combinations

## Slide 9: ENERGY SECURITY EXAMPLES
Different:
Causes
Components
Time
Space

## Slide 10: Security: who for?
Whose security? Which segments of human populations in space and time?
Which segments of the world populace? Which countries, which social classes, which genders, etc.?
Security when? Now, next year, in 50 years, in 100 years?
Do some energy security measures improve security for one segment in space-time but degrade security for another segment in another space-time?
All people all of the time? Present and future generations of the world populace.
All people some of the time? The world populace now.
Some people in one country now? Motorists in the UK?

## Slide 11: Scope: temporal and spatial
AIM: assess options for the security of energy services for the UK
TIME: security issues very time dependent
Horizon? : 2020, 2050, ultimately 100% renewable?
Time periods: hours/years/decades.
Rate of change: how fast can options be implemented?
How might short term security options undermine long term security? E.g. LNG wastes ~20% gas reducing future availability
SPACE:
Local
National
European
Global

## Slide 12: Some issues – human
Ethics
What is importance of convergence on equitable per capita CO2 and energy for negotiating global energy and climate protocols?
Should rich countries use more fossil fuels than necessary for their own security, so reducing developing countries future access to these resources?
How do irreversible security options (e.g. nuclear, CCS) limit decisions of future generations?
Politics
How will UK security options impact on global security? E.g. if UK has nuclear power, then how does this impact on negotiations with Iran or North Korea?
Labour
How vulnerable is technology operation to political action such as strikes?

## Slide 13: Some cross linking security issues
Energy and food
Biofuels vs food
Energy for food production
Energy and military
Civil nuclear programmes and weapons
Politics
How will UK security options impact on global security? E.g. if UK has nuclear power, then how does this impact on negotiations with Iran or North Korea?
Environment
Climate change
Energy and trade
Impact of oil shortage on trade with shipping and aviation

## Slide 14: Security : preliminary generalities
Supply security over different time scales
Gross availability of supply over future years. The main security is to reduce dependence on the imports of gas, oil and nuclear fuels and electricity through demand management and the development of renewable energy.
Meeting seasonal and diurnal variations. This mainly causes difficulty with electricity, gas, and renewables except for biomass. Demand management reduces the seasonal variation in demand and thence the supply capacity problem for finite fuels and electricity. Storage and geographical extension of the system alleviates the problem.
Security of economic supply.
Demand management reduces the costs of supply.
  The gross quantities of fuel imports are less, and therefore the marginal and average prices
  The reduced variations in demand bring reduced peak demands needs and therefore lower capacity costs and utilisation of the marginal high cost supplies
The greater the fraction of renewable supply, the less the impact of imported fossil or nuclear fuel price rise
A diverse mix of safe supplies each with small unit size will reduce the risks of a generic technology failure
Security from technology failure or attack. In the UK, the main risk is nuclear power.
Security from irreversible technology risk. In the UK, nuclear power and carbon sequestration
Environment impacts. All energy sources and technologies have impacts, but the main concern here are long term, effectively irreversible, regional and global impacts. The greater the use of demand management and renewable energy, the less fossil and nuclear, the less such large impacts.

## Slide 15: Security : electricity
Demand management will reduce generation and peak capacity requirements as it :
reduces total demand
reduces the seasonal variation in demand, and thence maximum capacity requirements
Load management can contribute to the matching of demand with variable supply with storage, control and interruptible demand.
Dispatchable generation
In the UK, existing and new fossil or biomass generators could be used to meet any deficit of CHP and renewable electricity supply. Currently there are about 55 GW of main fossil stations, and 5-10 GW of private generators. A fraction of these could be retained for the long term future, depending on the economics.
Currently in the UK, there are these capacities:
  Coal 19 GW large domestic coal reserve
  Oil 4.5 GW oil held in strategic reserves
  Dual fired 5.6 GW
  Gas 25 GW gas availability depends on other gas demands
Utilisation, if necessary of some end use sector generation. Currently in excess of 7 GW, but some of these plants are less flexible because they are tied to end use production, services and emergency back-up
Generators with liquid fuels which may be stored for times of deficit. These plant would not then subject the gas supply system to a peaky demand.
The building of new flexible plant such as gas turbines if large stations are not suitable
Role of biomass CHP with heat storage
Electricity trade with other countries can be used for balancing. There are geographical differences in the hourly variations of demands and renewable supply because of time zones, weather, etc. The strengthening of the link between France and the UK, and creation of links with other countries would enhance this option.

## Slide 16: Security : can we quantify to aid planning?
What is the optimum balance?
Within infrastructure:
Transmission
Storage
Conversion capacity
Between infrastructure and other security measures:
Demand management – efficiency and load management
Renewable energy
The modelling challenge
Technical: dynamic spatiotemporal systems modelling at short time periods over many countries
Other dimensions; economic, political, environmental

## Slide 17: Energy security model - system
A very simple illustrative service chain:
delivers 3 types of service – emergency, economic and leisure each with a different economic value per unit of energy
has 3 renewable sources, 2 distribution links, 1 store, each with an economic cost
This system operates in across time periods (minutes, hours, days…)
Each individual component has a probability of:
Initial failure in a time period
Continuing failure in subsequent time periods (e.g. probability of being mended) - autocorrelation
Additionally, renewables have non-random probabilities of intensity – most renewables have natural cycles.
[These probabilities might be dependent – i.e. probability of failure of 1 component is dependent on another, or covariant on an exogenous factor (e.g. weather), but this is not modelled here.]

## Slide 18: Energy security model – system operation
The chart shows the variation over a sample time of:
Energy service demands (shaded areas) and supplies (red line)
Primary supply (blue line)
Storage (black squares)
Unserved energy service of supply (columns)
Note: this a system with a high probability of service loss for illustration

## Slide 19: Energy security model – system operation
This animation (it should run automatically) shows random sampling of a given number of time periods.
[You may need to enable playback]

## Slide 20: Energy security model – simulation sample
The model can then be run many times over a period of time with random probabilities.
The probability of different percentages of energy being unserved on average of the period is then found.
This is shown in the charts for emergency,, economic and leisure services.
.
In this chart, the probability of 15 % of energy being unserved is about 50% for leisure, 20% for economic, and 0% for emergency
In these, the probabilities of unserved services decrease as storage capacity is increased

## Slide 21: Energy security model – optimisation
The system can then be optimised by finding the least total cost over time of :
Service, both served and unserved. Different services have different values: e.g. emergency 1000 p/kWh, economic, 12 p/kWh and leisure 5p/kWh.
The components of energy supply with different capital and operating costs.
The optimisation adjusts decision variables for the capacities of the supply chain components to find the minimum value of the objective function. In this example, the values and capacities of the optimum system components are as follows:

## Slide 22: Energy security model – optimisation, loss of service
The optimised system can then be simulated and sampled to give loss of service probability distributions.

## Slide 23: Energy security model – discussion
The system modelled is simple, but the approach shows proof of concept; a possible means to technically and economically quantify security and resilience. The approach is not entirely new (e.g. see Loss of Load Probability calculations in conventional electricity systems), but it has some novelty in some respects:
The model is dynamic
Different services with different values are modelled
Storage is explicitly included
Variable renewable sources are included
The model could be used to explore the security and resilience of the energy service system against: different types of failure (climate, technological, social etc.) with different probabilities, and over timescales from days to years.
The simulation and optimisation could be extended to include:
Control strategies
System configuration.
The inclusion of new components, multiple energy forms and different network configurations

## Slide 24: Sankey 2005

## Slide 25: UK Energy flow chart: Animation 1990 to 2050

## Slide 26: UK Energy flow chart: 2050

## Slide 28: World energy : gas reserves
IndexMunid
Definition: This entry is the stock of proved reserves of natural gas in cubic meters (cu m). Proved reserves are those quantities of natural gas, which, by analysis of geological and engineering data, can be estimated with a high degree of confidence to be commercially recoverable from a given date forward, from known reservoirs and under current economic conditions.

## Slide 29: World energy : BP (2008) Oil R/P

## Slide 30: World energy : Oil what’s left

## Slide 31: Oil Flows & Major Chokepoints: The “Dire Straits”
The risk of an oil-supply disruption will grow as trade & flows through key maritime & pipeline chokepoints expand
Notes: Increased trade will intensify worries about the world’s vulnerability to oil-supply disruptions, as much of the additional trade will involve transport along routes that are at risk of sudden closure – so-called chokepoints.
Some of the principal maritime routes that oil and LNG tankers are obliged to follow have narrow sections that are susceptible to piracy, terrorist attacks or accidents.
The 2 main chokepoints are the Straits of Hormuz at the head of Persian Gulf and the Straits of Malacca in southeast Asia – the dire straits. More than 26 mill bbls flow through these two chokepoints every day. A disruption in supply at either of these points could have a dramatic impact on oil prices.

## Slide 32: Proved oil reserves

## Slide 33: Oil consumption per capita

## Slide 34: World energy: uranium reserves
http://www.wise-uranium.org/umaps.html

## Slide 35: Energy, Environment and Security Europe Mark Barrett Mark.Barrett@ucl.ac.uk University College London

## Slide 36: Outline
EU scenarios: finding low/least cost strategies to meet security, climate and air pollution objectives
People, demand and management in energy scenarios
EU Energy scenarios. EU scenarios with different demand and supply measures.
Trade flows. Imports and exports of energy across EU boundary
Trade. Implications for security
Need for further analysis
Comments on security

## Slide 37: Energy is for services for people Exogenous assumptions (from PRIMES WCLP scenario): basic drivers
Population peaks and declines
More households
GDP growth (ha ha!)

## Slide 38: Energy services

## Slide 39: Ethics: equal CO2 emission per person?
Humans have equal rights to emissions, therefore convergence of emission per person in the EU and elsewhere? What about different resources and climate of countries? Note that for global equity, EU per capita emissions will have to fall by over 95% to reach 60% reduction globally.

## Slide 40: Objectives, instruments and measures

## Slide 41: Energy measures
Measures that reduce finite fuel consumption and atmospheric emissions. Mix of measures can be applied to different degrees at a ‘natural’ rate (years); note the general rapid rate of introduction of behavioural/operational measures which helps meet near term targets (e.g. 2020).

## Slide 42: The importance of demand measures
Chart shows UK national CO2 as a proxy for fossil fuel consumption
Demand measures:
Reduce upstream energy
Some cause rapid reduction with large effect on energy, carbon emission and warming integrated over years, therefore enhance security
Chart illustrates integrated global warming reduction 2010-2030 for demand management measures

## Slide 43: SEEScen sample: EU25 CO2 : variant scenarios
40% reduction
New nuclear
Maximum behaviour
No new nuclear
Maximum technology
No new nuclear
Maximum technology and behaviour
No new nuclear

## Slide 44: SEEScen sample: energy security
EU25 cross border energy trade : including fuels for international transport: EU30pc20N scenario
Declining finite fossil and nuclear imports
Increasing export of (mainly) renewable electricity
Energy exchange

## Slide 45: Trade and security
International transmission for the exchange of renewable electricity, enhances security and reduces costs, because:
Different availabilities of low carbon energy sources
Geographical dispersion benefits demand and renewable diversity
Possibility that the EU exchanges renewable electricity for gas from Russia etc.
Exchange of energy enhances security through co-dependency.
International transmission for the exchange of renewable electricity, enhances security and reduces costs
Animation shows trade model optimising for one period

## Slide 46: Possibilities for development
The social, physical, technological and economic fundamentals
Improved data on:
  social drivers of demand
  energy demand technologies - buildings, transport etc.
  geographical and temporal availability, distributions and costs of renewable, fossil and fissile energy resources
Better national scenario modelling
Energy system transport/transmission and storage requirements
Global scenarios and trade model – simulation and optimisation

## Slide 47: Resources: General
General
Matthew H. Brown, Christie Rewey, Troy Gagliano; 2003; Energy Security; National Conference of State Legislature. ISBN 1-58024-287-1. http://www.oe.netl.doe.gov/docs/prepare/NCSLEnergy%20Security.pdf
Hans-Holger Rogner1, Lucille M. Langlois2, Alan McDonald3, Daniel Weisser4, Mark Howells5, 2006, THE COSTS OF ENERGY SUPPLY SECURITY / LA SÉCURITÉ DES APPROVISIONNEMENTS ÉNERGÉTIQUES, International Atomic Energy Agency, Planning and Economic Studies Section. 27 December 2006. http://www.iaea.org/OurWork/ST/NE/Pess/assets/Energy_Security_WEC_paper070123.pdf
World Economic Forum, Cambridge Energy Research Associates; 2006; The New Energy Security Paradigm. http://www.weforum.org/pdf/Energy.pdf
Definition
http://www.oe.netl.doe.gov/docs/prepare/NCSLEnergy%20Security.pdf
http://www.mees.com/postedarticles/oped/v50n45-5OD01.htm
Human / political
http://www.isdp.eu/research/energy-security-and-cooperation.html
Ethical
http://www.unescobkk.org/rushsap/energyethics/eetwg7/
http://www.ogel.org/article.asp?key=2629
Economic
http://www.cepen.org/download/71/
http://www.roubini.com/topic/energy-security-and-supply-risks.php
http://papers.ssrn.com/sol3/papers.cfm?abstract_id=1522323
Terrorism
http://www.foreignaffairs.house.gov/archives/109/22655.pdf
http://www.ensec.org/
http://www.iags.org/archive.htm
http://www.isodarco.it/courses/andalo07/paper/andalo07_Ercolani_paper.pdf
http://www.apec.org/etc/medialib/apec_media_library/downloads/ministerial/sectoral/energy/20040.Par.0019.File.v1.1
http://spinprofiles.org/index.php/The_International_Terrorism_and_Energy_Security_Conference

## Slide 48: Resources: Barrett
Barrett M, December 2007, Low Emission Energy Scenarios for the European Union, report 5785. ISBN 91-620-5785-5, ISSN 0282-7298. http://www.naturvardsverket.se/Documents/bokhandeln/620-5785-5.htm
Naturvårdsverket (Swedish environmental protection agency, SE-106 48 Stockholm www.naturvardsverket.se
Low Emission Energy Scenarios for the UK - a transition to a secure, renewable low emission future. www.iiasa.ac.at/rains/meetings/Aspiration2050/Presentations/Session%204/Barrett.ppt
Renewable electricity system: Feasibility of a high renewable electricity system
Barrett, M. 2007, A Renewable Electricity System for the UK. In Renewable Energy and the Grid: The Challenge of Variability, Boyle, G., London: Earthscan. ISBN-13: 978-1-84407-418-1 (hardback).
http://www.cbes.ucl.ac.uk/projects/energyreview/Bartlett%20Response%20to%20Energy%20Review%20-%20electricity.pdf
http://www.bartlett.ucl.ac.uk/markbarrett/Energy/UKEnergy/UKElectricityGreenLight_100506.ppt
Consumption: Report on consumption, energy and carbon dioxide including behavioural measures.
http://www.bartlett.ucl.ac.uk/markbarrett/Consumption/EneCarbCons05.zip
Aviation:
Technical scenarios http://www.bartlett.ucl.ac.uk/markbarrett/Transport/Air/Aviation94.zip
Effects of taxes: http://www.bartlett.ucl.ac.uk/markbarrett/Transport/Air/AvCharge.zip
Transport:
Overview of some aspects of sustainable transport : http://www.bartlett.ucl.ac.uk/markbarrett/Transport/TransportSus_MBarrett_020608.ppt
Consultancy to DfT on project. Carbon Pathways: Analysis Informing Development of a Carbon Reduction Strategy for the Transport Sector, July 2008 .http://www.dft.gov.uk/pgr/sustainable/analysis.pdf
Summary presentation of some Auto-Oil work on transport and air quality, including some non-technical measures: http://www.bartlett.ucl.ac.uk/markbarrett/Transport/Land/AutoOil/JCAPWork.ppt