## Slide 1: Optimization for energy and environment systems technology and policy - some practical advice and examples Mark Barrett Mark.Barrett@UCL.ac.uk November 2010

## Slide 2: INTRODUCTION
This is some practical advice for optimising society, energy and environment systems with quantitative techniques.
Optimisation can sometimes aid the design of these systems to meet policy objectives efficiently and at low cost.
This is simply an informal introductory presentation of some aspects of optimisation. It is not intended to be comprehensive, or mathematical.
To watch animations, the presentation needs to be run (e.g. with F5).

## Slide 3: SYSTEM, MODEL, SIMULATION, OPTIMISATION
The system considered is a society energy and environment system. It always has a physical element, but may also have human elements such as cost. It may extend beyond energy demand and supply to the environmental or human health systems.
The system can:
Extend in size from a light bulb to an occupied building to a global trading system
Have processes which are significant over seconds, hours, years or centuries
A model simulates some inanimate physical and/or human features and processes of the system.
Generally the simulation requires complex sets of equations, often iterated, that are not amenable to algebraic solution and thence manual optimisation.
A model is used to explore new possible system configurations and states in order to aid the development of systems and policies..
One optimises the system by finding combinations of system changes (physical measures, economic instruments, etc.), called decision variables, that will minimise (or maximise) some aspect(s) of system performance, called the objective function, subject to constraints.
The objective function can be total cost, or efficiency, or some composite penalty function including cost, carbon emission, size etc.

## Slide 4: OPTIMISATION: PROBLEM TYPES AND METHODS
Problem types – usually related to system simulation
Discrete / continuous
Linear / non-linear
Static / dynamic
Single / multi objective
Recipe, order, scheduling, combinatorial problems etc.
There are many many techniques.
http://en.wikipedia.org/wiki/Optimization_%28mathematics%29
Some common optimisation techniques used for energy systems:
Linear programming (LP) for continuous linear systems
Hill climb / steepest descent for continuous linear or non-linear systems
Genetic, particle swarm and other biological algorithms for most types of problem
Choose the appropriate technique for the problem for best speed and accuracy.
Multiple techniques can be used iteratively for some problems.
For some problems specially tailored techniques can be more efficient (finding good solutions with fewer calculations) and accurate.

## Slide 5: SOME NICE AND NASTY PROBLEMS
In the pitch dark, you are parachuted into a field. How do you find the lowest spot?
How does prior knowledge help?
Nice. Just step downhill.
Not so nice. For these need to restart in different places
in the hope of starting on a slope to a global minimum..
Multiple minima. Might start in global minimum valley
Nasty. No gradient, might stumble on broad minimum.
Very nasty. No gradient, might stumble on narrow minimum.

## Slide 6: SOME OBSERVATIONS
All knowledge is approximate. Optimisation for developing energy technologies and policy often require highly uncertain assumptions about the future.
To improve confidence in the robustness of optima, sensitivity/Monte Carlo etc analysis can be used, but these often on subjectively assumed distributions.
It is often not known if there are several ‘local’ optima, or certain that the best has been found.
Marginal improvements in the objective function often rapidly decrease with more optimisation model evaluations.
Sharp optima are almost always wrong for SEE systems.
Optima are usually broad allowing decisions to take account of factors and criteria not included, not reliable or not quantifiable in simulation or optimisation modelling.
Measures appearing in optimum configuration may appear, disappear, reappear depending on constraints such as emission limit.

## Slide 7: OPTIMISATION: SOFTWARE AND HARDWARE
Any programming language can be used for simulation and optimisation.
Common software: Excel/VBA, Matlab, GAMS, FORTRAN, Python etc. can all be used to build simulation models. These can generally be used together directly or via some standard exchange format such as Excel.
Most common software has optimisation programmes that will address standard optimisation problems; some is free (e.g. Excel, Matlab), some is commercial, though there may already be a site licence.
Multiple optimisation methods can be applied to many problems.
Some software requires programming skills, some (like Excel optimisation packages) do not.
Sometimes it is possible to use a pre-existing simulation model and apply separate optimisation software to it.
If you want others to use or access your model, bear in mind, :
the most common installed and used software is Microsoft Office and that Mac versions may not have all the features of Window versions, though emulation can be used.
the memory and speed limitations of typical PCs

## Slide 8: OPTIMISATION: SOFTWARE
A small selection of optimisation software. Some of it can operate in several computer/operating system environments (Excel, Matlab etc.) and some may be incorporated into user written programmes.
General
http://en.wikipedia.org/wiki/List_of_optimization_software
http://www.mat.univie.ac.at/~neum/glopt/software_g.html
Excel:
Free with Excel: Solver useful for small problems
Commercial: Frontline http://www.solver.com/
Matlab
http://www.mathtools.net/MATLAB/Optimization/index.html
Commercial: http://www.mathworks.com/products/optimization/
GAMS
Commercial: http://www.gams.com/
Commercial
http://www.lindo.com/
http://www.fico.com/en/Products/DMTools/Pages/FICO-Xpress-Optimization-Suite.aspx
http://www.mosek.com/
g

## Slide 9: SOME EXAMPLES
Examples in bold included in presentation.
Demand vs supply marginal cost curve
Building
Ship speed
Shipping network
National energy system
  MARKAL
  SEE_Opt
Trade
Energy security
Electricity systems
  Configuration
  Dynamic management
Transport. Air pollution control
Challenging problems
  Energy space time modelling
  Dynamic transport network
  Multi agent ‘emergent’ optimal control of energy systems

## Slide 10: MARGINAL COST CURVES
Find least cost combination of demand and supply.
Develop Marginal Cost Curves (MCCs).
  Estimate the unit cost (£/GJ, £/tCO2) of changing flows with individual measures (insulation, wind turbine etc.)
  Order them by increasing unit cost
Reduce demand from 1 with energy efficiency, marginal cost increases
Increase supply from 0, marginal cost increases
Total cost is sum of energy efficiency and supply costs
The least cost optimum is where marginal cost curves cross.
Nice and simple?

## Slide 11: MARGINAL COST CURVES: cautions and limitations
The effects and cost s of measures only relate to a particular system at particular time. For example, increasing insulation in the current gas-heated UK housing stock might reduce its CO2 emission by 20%; if the houses were 100% heated with renewable electricity the reduction would be 0%, though there would probably be cost savings through insulation.
Measures are synergistic. E.g. insulation reduces energy consumption by x% and a heat pump by y%, together they reduce consumption by 1-[(1-x)(1-y)]% which is always less than (x+y)%. If each measure saves 50%, total savings are 75% not 100%. So the effects of measures can often not be simply summed across the curve.
Measures can ‘appear’ and ‘disappear’ in curves. For example, a condensing boiler reduces CO2 emission by 20% for 1 £/unit CO2, a heat pump by 50% for 3 £/unit – these are mutually exclusive options for a dwelling. For 20% the boiler is least cost; for 50% the heat pump would be used rather than the boiler which would ‘disappear’ from the curve. It can even be that measures will reappear for larger reductions.
Energy systems are dynamic, always changing with time. A simple illustrative example: annual demand is 400 TWh and we have two energy sources: wind which can produce 1000 TWh at 10 p/kWh; solar PV can produce 500 TWh at 30 p/kWh. So obviously all wind as it’s cheapest? Sadly, another fact is that there is insufficient wind in the summer and so solar PV must be used then. Marginal costs for individual measures are often misleading – it is system marginal costs that are critical and this is hard to determine in dynamic systems.
Costs and benefits are often evaluated using Net Present Valuation which uses discount or interest rates which are, to a degree arbitrary and different for different economic agents . The NPV of a measure will change with discount rate and this can alter the ordering of measures by unit cost on the marginal cost curve.
Limitations 1-4 are why whole system optimisation is useful – the costs of individual measures are input but the marginal system costs emerge from the optimisation. Some of these issues are illustrated below.

## Slide 12: NATIONAL SYSTEM
Find least cost configuration energy demand and supply system based on annual energy.
Simulation: a toy model.
Objective: least cost
Constraints: maximum carbon emission, fuel availabilities
Decision variables: energy efficiency, energy production
Problem type: non-linear continuous
This model:
  Has separate cost curves which may therefore be summed, for:
  each demand (heat, transport, electricity)
  each secondary supply (heat, electricity)
  each primary supply (fossil, nuclear, renewable)
Accounts for some non-linear synergies
Does not account for any dynamics

## Slide 13: NATIONAL SYSTEM: cost curves
Energy supply
Useful energy demand reduction

## Slide 14: NATIONAL SYSTEM: decision variables
Energy supply
These are the decision variables that are adjusted during optimisation.
For heat and transport, useful energy demand and fuel mix are changed.
For CHP and electricity, the fuel mixes are changed.

## Slide 15: NATIONAL SYSTEM: optimisation animation
This shows the effect of changing decision variables on energy, emissions and cost.
The optimiser panel is shown on the left..

## Slide 16: BUILDING
Find least cost combination of building shape, energy efficiency and energy system given a public energy supply price.
Objective: least cost
System: non-linear continuous
Constraints: volume
Decision variables: shape, insulation, ventilation, heating system efficiency

## Slide 17: Individual building optimisation animation showing effect of different fuel price on optimum

## Slide 18: ELECTRICITY SYSTEM : CONFIGURATION OPTIMISATION
Find least cost configuration electricity demand and supply system accounting for the hourly dynamics of demand, supply storage and trade.
Objective: least cost
Constraints: minimum renewable energy fraction
Decision variables: generator and storage capacities
Problem type: non-linear continuous

## Slide 19: VarInt : Optimised system : demand and technology details
The table below shows some details of the optimised system. Yellow cells contain assumptions; those with bold type are the values changed by the optimiser. The tan cells contain minimum and maximum allowable values. Of note are the energy generated, the capacity factors, and the unit cost of electricity generation shown in the last row.

## Slide 20: VarInt : Optimisation: year graph animated
The animation shows the year sample as the optimiser seeks the least cost mix of supply and storage for fixed weather and renewable resources.

## Slide 21: ELECTRICITY SYSTEM : DYNAMIC ENERGY MANAGEMENT
System: very complex thermal generation dynamics, and demand with storage modules
.
Objective: Find least cost diurnal hourly operational strategy of given demand-generation system using demand management and dispatchable generation
Constraints: technology capacities
Decision variables: storage operation
Problem type: non-linear continuous
Method: specifically tailored iterative programme

## Slide 22: Electricity : animated load management optimisation

## Slide 23: ENERGY SYSTEM SECURITY
Find least cost system configuration given values of different services.
Objective: least cost
Constraints:
Decision variables: technology capacities
Problem type: non-linear continuous

## Slide 24: Energy security model - system
A very simple illustrative service chain:
delivers 3 types of service – emergency, economic and leisure each with a different economic value per unit of energy
has 3 renewable sources, 2 distribution links, 1 store, each with an economic cost
This system operates in across time periods (minutes, hours, days…)
Each individual component has a probability of:
Initial failure in a time period
Continuing failure in subsequent time periods (e.g. probability of being mended) - autocorrelation
Additionally, renewables have non-random probabilities of intensity – most renewables have natural cycles.
[These probabilities might be dependent – i.e. probability of failure of 1 component is dependent on another, or covariant on an exogenous factor (e.g. weather), but this is not modelled here.]

## Slide 25: Energy security model – system operation
The chart shows the variation over a sample time of:
Energy service demands (shaded areas) and supplies (red line)
Primary supply (blue line)
Storage (black squares)
Unserved energy service of supply (columns)
Note: this a system with a high probability of service loss for illustration

## Slide 26: Energy security model – optimisation
The optimisation adjusts decision variables for the capacities of the supply chain components to find the minimum value of the objective function – the value of service (or loss thereof) plus the cost of system technologies .
In this example, the values and capacities of the optimum system components are as follows:

## Slide 27: ENERGY TRADE
Find least cost system flow pattern given demands and supply costs.
Objective: least cost
Constraints: generation and trade link transmission capacities
Decision variables: link flows
Problem type: linear continuous

## Slide 28: Trade and security
International transmission for the exchange of renewable electricity, enhances security and reduces costs, because:
Different availabilities of low carbon energy sources
Geographical dispersion benefits demand and renewable diversity
Possibility that the EU exchanges renewable electricity for gas from Russia etc.
Exchange of energy enhances security through co-dependency.
International transmission for the exchange of renewable electricity, enhances security and reduces costs
Animation shows trade model optimising for one period

## Slide 29: SETTING EU EURO VEHICLE AND FUEL STANDARDS
Find least cost combination of measures to achieve air quality standards in European cities and set Euro III/IV vehicle emissions and fuel quality standards
Objective: least cost
Constraints:
Decision variables: discrete vehicle emission control and fuel quality packages
Problem type: discrete combinatorial
Method: bespoke multi-objective list ordering
Note that in the increasing system cost curve that measures ‘pop in and out’ of the least cost mix.

## Slide 30: European Auto Oil Programme modelling and optimisation process
For each city :
Set the urban emission reduction targets.
Input the urban traffic and emission data for the country in which the city is located..
Use TransOpt to estimate the stock turnover and fleet emission fractions by vintage in 2010 for the different vehicle categories.
Use TransOpt to find the least cost combination of technical mechanisms (vehicle, fuel and I&M packages) which achieves the required emission reduction.
Apply the least cost combination to each of the 12 EU States and so estimate the total EU cost of that combination, and the emission reductions achieved in each State.

## Slide 31: Overall package ordering and cost

## Slide 32: EU package combinations example Note packages can appear, disappear and reappear